## Slide 1: Current Code Structure
Similar to gPMC:
Start
Prepare data and transfer to computation device
Allocate memories for counters and stacks
Enough primary carbons simulated?
No
Yes
Perform statistics and transfer data to CPU
End
Load primary carbons
Load secondary particles and clear corresponding memories
Simulate loaded carbons and put generated secondary particles into secondary particle stack
nSecondary > nBatch ?
Yes
No

## Slide 2: Carbon Transport Kernel
Sample a step length
Cross voxel ?
Yes
Move to next voxel boundary and deposit dose
Move the sampled step, deposit dose and sample a hard event
No
Ionization
Sample energy of the delta electron and locally deposit
Nuclear 1
Sample energy of secondary particles and push it to stack
Nuclear 2
Sample energy of secondary particles and push it to stack
… …
Enough energy ?
Yes
No
Locally deposit remainder energy

## Slide 3: Physics Data
Restricted stopping power in water
Macro cross sections of hard events
Mass stopping power ratio
Differential cross sections
Calculated according to Bethe-Bloch Eq. and corrections (Kawrakow I 2000 Accurate condensed history Monte Carlo simulation of electron transport: I. EGSnrc, the new
EGS4 versionMed. Phys.27485–98)
Ionization cross section Calculated. Hadronic interaction data needed for significant channels.
Data needed for carbon and secondary particles to calculate deposited energy.
Data needed for carbon and secondary particles to sample energy and angular distributions after hadronic interactions.